## Slide 1: Mobile Computing

## Slide 2
Introduction to Mobile Computing
Challenges in Mobile Computing
Coping with Uncertainties, Poor Resources, Bandwidth
Cellular Architecture.co-channel Interference
Frequency reuse, Capacity Increase by cell Splitting, numerical on Frequency reuse
Evolution of Mobile System: CDMA,FDMA,TDMA, numerical on CDMA
GSM Architecture
Handoffs-types of handoffs
Location Management
Hierarchical Scheme
Predictive Location Management Schemes
Mobile IP
Case Study of CODA

## Slide 3: Mobile Computing: Introduction

## Slide 4: Natural Evolution of Computing
Freedom from Collocation
More
Flexible
Resource
Usage
Single User OS
Batch
Timesharing
Networking
LANs + WSs
Mobile Computing

## Slide 5: Why Mobile Computing ?
People are mobile
Devices are mobile

## Slide 6: What is Mobility?
A person who moves
  Between different geographical locations
  Between different networks
  Between different communication devices
  Between different applications
A device that moves
  Between different geographical locations
  Between different networks

## Slide 7: What is SAR
SAR Value is a measure of the maximum energy absorbed by a unit of mass of exposed tissue of a person using a mobile phone, over a given time or more simply the power absorbed per unit mass
Hint: Specific Absorption Rate

## Slide 8: Computing & Computation
Mobile Computing
  When User is Mobile
Mobile Computation
  When Computation is Mobile

## Slide 9: What is Mobile Computing?
The provision and utilization of a computing environment that a user can access and use (such as to communicate and to access remote information and services) anywhere and anytime

## Slide 10: Mobile Computing: What is not mobile computing?
Activity using mobile phones from anywhere in the world is not called Mobile computing - because there is no computing (data processing) involved
Dragging around a laptop and working with it without being able to set up a connection to the “home base” through a computer network is not Mobile computing

## Slide 11: Mobile Computing: What mobile computing requires?
Does Mobile computing require some devices to be dragged around by the people? Not necessarily, an infrastructure with suitable access devices could be offered to traveling people - in the same manner as telephones are offered in hotels, airports, etc.
Global networking infrastructure, but in this context especially the wireless access technologies are very important

## Slide 12: Mobile devices
performance
Pager
tiny displays
receive only
simple text messages
Mobile phones
voice, data
simple text displays
PDA
graphical displays
character recognition
simplified WWW
Palmtop
tiny keyboard
simple versions of standard applications
Laptop
fully functional
standard applications
Sensors,
embedded
controllers

## Slide 13: Mobile Applications - 1
Vehicles
  Transmission of news, road condition etc
  Ad-hoc network with near vehicles to prevent accidents
Emergencies
  Early transmission of patient data to the hospital
  Ad-hoc network in case of earthquakes
  Military

## Slide 14: Mobile Applications - 2
Travelling salesmen
  Direct access to central customer files
  Consistent databases for all agents
  Mobile office
Web access
  Outdoor Internet access
  Intelligent travel guide with up-to-date location dependent information

## Slide 15: Mobile Applications - 3
Location aware services
  Find services in the local environment, e.g. printer
Information services
  Push: e.g., stock quotes
  Pull: e.g., nearest cash ATM
Disconnected operations
  Mobile agents, e.g., shopping
Entertainment
  Ad-hoc networks for multi user games

## Slide 16: Mobile Applications - 4
Information Services (Yellow Pages)
Law Enforcement and Medical Emergencies
Sales and Mobile Offices
Weather, Traffic, Sports, Entertainment

## Slide 17: AI Cameras?
AI cameras are simply cameras that use AI programs to wisely deal with images and videos. Computational photography is usually the core of an AI-powered camera.

## Slide 18: Some Issues
Mobility
Wireless medium
Portability of mobile element

## Slide 19: Mobility
The location of mobile elements and therefore their point of attachment to the fixed network change as they move
Mobility of nodes
  Loss of connectivity
  Network partitioning;
  Bit errors.
  Configuration
  Location management
  Heterogeneity
  Security and authentication
  Hidden & Exposed terminal

## Slide 20: Configuration
  In designing distributed algorithms, we can no more rely on a fixed topology.
  The center of activity, the system load, and locality change dynamically.

## Slide 21: Location management
The search cost to locate mobile elements is added to the cost of each communication involving them.
Efficient data structures, algorithms, and query execution plans must be planned for representing, managing, and querying the location of mobile elements, which is a fast changing data

## Slide 22: Heterogeneity
Connectivity becomes highly variant in performance and reliability.
The number of devices in a network cell changes with time, and so do both the load at the base station and bandwidth availability.
There may be also variability in the provision of specific services, such as in the type of available printers or weather reports.
The resources available to a mobile element vary

## Slide 23: Wireless Medium
Wireless networks are more expensive, offer less bandwidth, and are less reliable and face many obstacles because the surrounding environment interacts with the signal
Data transmission over the air is currently monetarily expensive
Variant Connectivity
Tariffs

## Slide 24: Variant Connectivity
Wireless technologies vary on the degree of bandwidth and reliability they provide.

## Slide 25: Tariffs
For some networks (e.g., in cellular telephones), network access is charged per connection-time, while for others (e.g., in packet radio), it is charged per message (packet)

## Slide 26: Portability of Mobile Elements
Mobile element’s resource are poor when compared to static elements
Mobile elements rely on battery.
Mobile elements are easier to be accidentally damaged, stolen, or lost.

## Slide 27: Characteristics of mobile elements
Frequent disconnections
Predictable disconnections
Asymmetry
Monetarily expensive
Relatively unreliable
High bandwidth variability
Low bandwidth

## Slide 28: Characteristics of mobile communications
Limited resources
Limited memory
Limited computational power
Small screen
Limited battery life
Relatively unreliable
Variability in resources
Frequent location updates